## Slide 1: Battery Management System - AFE Design Review
Team CuriousIC

## Slide 2: System Architecture
Capacitively-Coupled Instrumentation Amplifier (CCIA) { Chopper, DC Servo Loop (DCSL) }
Incremental Delta-Sigma (DSM) Analog-to-Digital Converter (ADC) { DSM Loop, Clock Generation}

## Slide 3: Top-Level System Schematic

## Slide 4: ADC Specifications
Cascade of Integrators with Feed Forward (CIFF) architecture
State reset after each conversion after each conversion enables sequential multi-cell measurement in BMS AFE
Parameter | Details
Order | 3rd
ENOB | > 16 bits
Sampling Frequency | 4MHz
Signal Bandwidth | 3.9kHz
OSR | 512
Quantizer | 1-bit

## Slide 5: ADC Schematics
The 3rd-order Delta-Sigma ADC employs a cascaded three-stage loop filter.
A switched-capacitor (SC) analog adder combines the outputs of the integrators.
A 1-bit quantizer converts the summed analog signal into a digital output.

## Slide 6: ADC Schematics
Schematics of Integrators used in the DSM Loop Filter
1st Integrator
2nd Integrator
3rd Integrator

## Slide 7: ADC Schematics
Schematics of the OTAs for designing integrators
Common Mode Feedback (CMFB) is reused for both OTAs
OTA for 1st Integrator
OTA for 2nd Integrator
CMFB circuit for both OTA

## Slide 8: ADC Simulation Results
The integrator stage outputs exhibit stable bounded behaviour with progressively reduced signal swing across successive stages, indicating proper loop operation and effective higher-order noise shaping
1st Integrator Output
2nd Integrator Output

## Slide 9: ADC Simulation Results
3rd Integrator Output
Quantizer Output
The third integrator output remains bounded throughout the simulation, demonstrating stable third-order loop dynamics while accumulating and shaping the quantization error
The 1-bit quantizer produces a binary bitstream that switches between the two output levels according to the input signal amplitude. The varying pulse density encodes the analog input while enabling high-order noise shaping

## Slide 10: ADC Simulation Results
NMOS switches are used for the VCM and VREFN paths, while the PMOS switch is used for the VREFP path to provide lower ron and faster settling
Transmission Gate (TG) switches are employed in the signal path to achieve a nearly constant and low ON resistance over the full input voltage range
The simulated Ron characteristics shown above verify the appropriate switch selection, ensuring low resistance, improved linearity, and accurate switched-capacitor operation

## Slide 11: ADC Simulation Results
ADC Output Spectrum
The FFT spectrum shows a prominent fundamental component at the input frequency and effective high-frequency quantization noise shaping characteristic of a third-order ΔΣ modulator. The achieved SNR of 107.49 dB and SNDR of 103.74 dB validate the proposed ADC architecture.

## Slide 12: CCIA Specification
Capacitive coupling for blocking large DC common mode (CM), high common mode rejection ratio (CMRR), and accurate closed-loop gain
Chopper stabilized for offset and noise cancellation
Parameter | Details
Current | 100uA
OCV/EIS Gain | 1/100 V/V
Chopping Frequency | 5kHz
Zin | 30MΩ
Offset Voltage | 1uV
Noise (0.1-10 Hz) | 10uVrms
CMRR | >100dB
PSRR | >90dB

## Slide 13: CCIA Schematics
Top level schematic of CCIA

## Slide 14: CCIA Schematics
Schematic of instrumentation amplifier

## Slide 15: CCIA Schematics
Differential opamp with chopper and CMFB circuit

## Slide 16: CCIA Schematics
Transistor level schematic of gm1, gm2 and CMFB stages for the instrumentation amplifier
gm1
gm2
CMFB

## Slide 17: CCIA Schematics
Top level schematic of DC servo loop

## Slide 18: CCIA Schematics
Schematic of the OTA used for the DSL integrator

## Slide 19: CCIA Schematics
Transistor level schematic of the OTA and CMFB
gm1

## Slide 20: CCIA AC response
Achieved EIS mode gain of 30dB and OCV mode gain of 0dB
EIS mode
OCV mode

## Slide 21: CCIA CMRR analysis
Achieved CMRR above 112dB at 100Hz

## Slide 22: CCIA PSRR analysis
Achieved PSRR above 164dB at 100Hz

## Slide 23
EIS Architecture
The DAC generates smooth, precise analog sine waves to inject controlled AC excitation signals into biological or battery tissue.

## Slide 24: EIS TestBench Schematic
Vref = 4.2V
Clk period = 100us Li battery is connected across VB+ and VB-

## Slide 25: Top level schematic of EIS
Excitation current = 10 - 15 mA

## Slide 26
2C - DAC Schematics
C1 = C2 = 1pF

## Slide 27
Buffer schematic
Intrinsic gain = 50db UGB = 2.5MHz

## Slide 28: Simulation result
Code (LSB-MSB) | Expected value (V) | simulated Value (V) | Error (V)
00000000 | 0 | 0.1 | +0.1
11111111 | 4.2 | 4.192 | -0.008
00000001 | 2.1 | 2.115 | +0.015
10101010 | 1.395 | 1.41 | -0.015
01010101 | 2.789 | 2.807 | +0.018
00001111 | 3.938 | 3.949 | +0.011
VLSB = Vref = 4.2 = 0.0164V 2^N 2^8

## Slide 29
Simulation plots
DATA_in=11111111 , Vout=4.2V
DATA_in=00000000 , Vout=0V
DATA_in=00000001 , Vout=2.1V
DATA_in=10101010 , Vout=1.41V
*LSB- >MSB

## Slide 30: Simulation plots
DATA_in=00001111 , Vout= 0.394V
DATA_in=11110000 , Vout= 0.41V

## Slide 31: test case of generating Sine wave

## Slide 32: Design Specifications for Opamp
No. | Parameter | Value
1. | DC Open Loop Gain | >70dB
2. | Unity Gain Bandwidth | >30MHz
3. | Phase Margin | >60̊
4. | VDD | 5V
5. | Input Bias Current | 5uA

## Slide 33: Opamp Schematic

## Slide 34: Open Loop Testbench

## Slide 35: AC Simulation Results
88dB
Typical Corner Results:
DC Open Loop Gain = 88.27dB
UGB = 52MHz
Phase Margin = 60.5̊

## Slide 36: Closed Loop Buffer Schematic
Programmable Gain
Mode_sel = 0, Gain = 1(Default)
Mode_sel = 1, Gain = 30

## Slide 37: Closed Loop Testbench

## Slide 38: Transient Simulation Results, Mode_sel = 0, Gain = 1
Unity Gain mode
Vin = 20mV p2p
Mode_sel = 0

## Slide 39: Transient Simulation Results, Mode_sel = 1, Gain = 30
Mode_sel = 1
Unity Gain mode
Vin = 20mV p2p
Vout = 612mV p2p
Gain = 30.86

## Slide 40: Summary
No. | Parameter | Value | Simulations Results
1. | DC Open Loop Gain | > 70dB | 88.27dB
2. | Unity Gain Bandwidth | > 30MHz | 52MHz
3. | Phase Margin | > 60̊ | 60.5̊
4. | Current Consumption |  | 435uA
5. | Settling Time |  | 30ns